## Slide 1
ML Fault Detection & Self-Healing in Telecom Networks
Technical overview — simulation, machine learning, and MAPE-K evaluation

## Slide 2
Purpose
End-to-end pipeline for proactive RAN fault detection in dense HetNet networks
Combines NS-3 simulation, ML classifiers (RF, LSTM, SVM), and MAPE-K autonomic control
Research question: Does ML proactive detection reduce MTTR and improve availability vs. reactive threshold monitoring?
Results are observed from simulation — no artificial blending toward target tables by default

## Slide 3
Real-World Operational Context
Simulation imitates Nigerian MNO operations (e.g. MTN, Airtel) — not a live network integration
Power fault → site outage (grid / generator / rectifier failure)
Congestion → peak-hour or event traffic surge
Hardware fault → RRU/BBU failure or transport cut
Reactive baseline: severe OSS-style thresholds, 240–300 min manual remediation
MAPE-K path: earlier ML detection, 35–55 min modelled automated recovery

## Slide 4
System Architecture
Stage 1: NS-3 HetNet simulation → per-cell KPI CSV files
Stage 2: Merge trials → kpi_master_dataset.csv
Stage 3: Sliding windows → train RF, LSTM, SVM
Stage 4: MAPE-K loop on test data → MTTR and availability
MAPE-K: Monitor → Analyse (ML) → Plan → Execute

## Slide 5
Network Topology (Table 3.1)
7 macro + 21 small cells = 28 cells total
Hexagonal layout, inter-site distance 500 m
500 UEs (design target); 280 UEs stable default on NS-3
300 s simulation; 1 s KPI interval
50 trials × 4 fault types = 200 simulation runs
Full dataset: ~1.68 million raw CSV rows

## Slide 6
Three Simulation Backends
thesis-fault-sim — fast KPI generator for large-scale ML datasets
thesis-fault-sim-lte — LENA LTE/EPC with real PHY traces + FlowMonitor
thesis-fault-sim-nr — 5G-LENA NR/EPC (n78, 3.5 GHz) for 5G validation
All backends use identical CSV schema and fault labelling
Commands: run_all_trials.py | --lte | --nr

## Slide 7
Fault Classes
0 — Normal: no active fault window
1 — Power fault: gNB transmit power collapse
2 — Congestion: UDP traffic surge on affected cell UEs
3 — Hardware failure: gNB PHY deactivation
Stochastic per trial: random cell, onset time, duration
Ground truth stored in fault_label column for supervised ML

## Slide 8
KPI Features (8 per cell per second)
RSRP, SINR, PRB utilisation
Downlink and uplink throughput
Packet loss rate, handover success rate, latency
Collected every 1 s for each of 28 cells

## Slide 9
Machine Learning Pipeline
10-second sliding windows, stride 1, per cell
48 tabular features (6 statistics × 8 KPIs) + sequences for LSTM
Train / val / test: 70 / 15 / 15 % stratified split
SMOTE on training data only; PCA 95% variance on tabular features
Models: Random Forest (tabular), LSTM (temporal), SVM (baseline)
Output: reports/ml_metrics.json (observed accuracy, F1, AUC)

## Slide 10
MAPE-K Evaluation
Monitor: KPI window pre-filter (PRB, RSRP, loss, throughput)
Analyse: ML inference with confidence threshold 0.70
Plan / Execute: fault-specific remediation (Table 4.6, minutes)
Compared against reactive baseline (severe thresholds only)
Outputs: MTTR and network availability per model
NCC 99% availability benchmark in Chapter 4 figures
Reference targets: Reactive ~312 min MTTR; LSTM ~102 min; availability ~99%

## Slide 11
Dataset Tracks
Track A — KPI generator: full scale, fast, simplified RAN physics
Track B — LTE: real LENA traces, LTE-A HetNet surrogate for 5G
Track C — Both: ML/MAPE-K on KPI data + LTE cross-validation
Document which backend produced each result set

## Slide 12
Key Outputs & Files
output/kpi_master_dataset.csv — merged labelled dataset
reports/ml_metrics.json — classifier performance
reports/mapek_summary.json — MTTR and availability
reports/fig3_*.png — Chapter 3 methodology figures
reports/fig4_*.png — Chapter 4 results figures
thesis_constants.py — approved parameters and reference targets

## Slide 13
Limitations
Simulation study — not live commercial RAN deployment
MAPE-K Execute models recovery time; no real OSS API integration
280 UE default due to NS-3 stability (500 is design target)
Some Chapter 3 figures are schematic methodology diagrams
NR trials require significantly longer runtime than KPI generator
Metric blend weight = 0 (observed-only reporting)

## Slide 14
Technology Stack
NS-3 3.38 — network simulator
LENA (LTE) + 5G-LENA v2.4 (NR) — RAN stacks
TensorFlow/Keras 2.15 + scikit-learn 1.5 — ML
imbalanced-learn — SMOTE
Pipeline: setup.sh → run_all_trials.py → preprocess_and_train.py → mapek_loop.py